## Slide 1: Raspberry Pi Master Class Day-2
Installing Operating System in RPi

## Slide 2: 01 Table of Contents 03 04 02
Startup with RPi
Starting with Raspbian
Rpi Operating System
List of Operating System
Discussion & Q&A
Interractive session
How to Install OS
Procedure to install OS in RPi

## Slide 3: PREREQUISITES FOR THIS COURSE
Raspberry Pi 3 Model b/B+
16 GB SanDisk class 10 SD Card
Card reader
Laptop with Internet
Power Adapter – 5V 2Amps
USB B-Type Cable

## Slide 4: Raspberry Pi OS Version

## Slide 5: Raspbian OS
Raspbian is a free operating system based on Debian optimized for the Raspberry Pi hardware.
An operating system is the set of basic programs and utilities that make your Raspberry Pi run.
However, Raspbian provides more than a pure OS: it comes with over 35,000 packages, pre-compiled software bundled in a nice format for easy installation on your Raspberry Pi.
The initial build of over 35,000 Raspbian packages, optimized for best performance on the Raspberry Pi, was completed in June of 2012.
However, Raspbian is still under active development with an emphasis on improving the stability and performance of as many Debian packages as possible.

## Slide 6: Download Raspbian…
https://www.raspberrypi.org/software/operating-systems/

## Slide 7: Software Required
RUFUS
Win32 disk Imager / Etcher

## Slide 8: Installing Operating System
Test with RPi
Download & Burn OS
Configuring Wifi info for Laptop access
Format SDCard
4
1
3
2

## Slide 9: Configuring WiFi…
ctrl_interface=DIR=/var/run/wpa_supplicant GROUP=netdev
update_config=1
country=IN
network={
ssid="ZTE-adde78"
psk="885dfbad"
}
Create File in root as wpa_supplicant.conf (Note: Without txt extension)
To Find COUNTRY CODE : https://en.wikipedia.org/wiki/ISO_3166-1

## Slide 10: Configuring WiFi…
Empty SSH File
Create File in root as ssh (Note: Without txt extension)
Insert SD Card to Pi and Power UP
Open Fing to find IP Address of Pi
Ssh ipaddress in Putty or Terminal
Putty : https://www.chiark.greenend.org.uk/~sgtatham/putty/latest.html
username : pi
password : raspberry

## Slide 11: Installing XRDP
Open Remote desktop
Enter Ipaddress
Enter Username & Password
sudo apt-get install xrdp

## Slide 12: Installing Python3 Idle
OpenTerminal
Enter above command
sudo apt-get install idle3

## Slide 13: Informative Interractive Interesting
Question/Day
Discussion on Next Day
Learn Science !
Daily Science Discussion

## Slide 14
Q1 – Discussion
Nikola Tesla
Photographic Memory
Alternating-current (AC)
Hydroelectric Power Plant
Tesla Coil
He wanted to illuminate the entire earth
Wireless transmission of power
Who invented Radio???????????

## Slide 15
Q2 – Discussion
Theory of Relativity

## Slide 16: Thanks!
learn.pantechsolutions.net
“BE ALONE, THAT IS THE SECRET OF INVENTION; BE ALONE, THAT IS WHEN IDEAS ARE BORN.”
www.pantechsolutions.net